Title
Meshing To Realistic Domains
Applied Modelling and Computation Group
http://amcg.ese.ic.ac.uk
By Mihai Jiplea, Shaun Lee, Elliot Lynch and Varun Verma

---
Introduction
  1. We were tasked with developing a user-friendly graphical interface for the meshing of realistic domains
  1. The method chosen was to create Python plugins for Quantum GIS (QGIS)
  2. Produced: Rasterise Polygons, RasterCalc and Mesh NetCDF

---
Domains
- Domains to be meshed are stored as Shapefile polygons
- QGIS can extract the domain from either bathymetric data or a Shapefile layer such as GSHHS

---
Obtaining Domain
  1. Extract the 0 m contour and create polygon(s) from the contour
  1. Add a boundary layer defining the extent of the domain

---
Obtaining Domain
  1. Perform a 'difference' vector operation to obtain the domain

---
Define Physical ID's
  1. We are able to define unique ID's for domain boundaries
  2. Distinct ID's allow separate boundary conditions to be used in Fluidity
  3. A layer is added with polygons defining the ID
  4. The part of the boundary lying underneath a polygon obtains that ID when the Geo file is created

---
Mesh-Size Metric
  1. The Mesh NetCDF plugin uses a NetCDF file as a mesh-size metric
  2. The value contained by the pixels define how fine the mesh element size shall be
  3. One example is mesh size related to depth – fine where shallow and coarse in deeper areas

---
Defining Mesh Metric
  1. Regions can be defined for specific mesh size
  2. Add a new layer above the bathymetry
  3. Each ID of the polygon represents depth in that area

---
Calculations with Rasters
  1. To combine the bathymetry and the specific mesh size raster we can use RasterCalc

---
Mesh Metric

---
Meshing
  1. Now there is a domain, boundary ID and mesh-size metric layer we are able to mesh
  2. Mesh NetCDF will create a Geo file and use the mesh-size metric as the background field

---
Mesh

---
Multiple Domains
  1. The plugin allows the meshing of multiple domains
  2. For example, meshing the ocean and ice shelf of Antarctica as separate domains

---
Antarctica Ocean and Ice Shelf Domains